## Slide 1: Lab Organizational Meeting
1/23/13

## Slide 2
General Lab Rules and Guidelines
Always close and lock the lab door if no one is inside.
If you see that a general lab supply is running low, write the catalog number, company, and quantity desired on the white board. Try to write items up far enough in advance to ensure we don’t run out.
Always wear gloves in lab. Also, please spray gloves with 70% EtOH before opening incubators.
Please notify Shelly of any problems ASAP.
You are responsible for your bench space’s cleanliness and waste.
Always close the sash of the chemical/fume hood when you are not working inside it.
Never wear gloves outside of the lab (please remove your gloves using the computer room or going to the offices).
Please wipe down the balances when you are done using them and return all chemicals to their proper shelves.
Please turn off orbital shakers, mixers, and the stripping water bath when not in use.
Make sure samples are capped tightly and counterbalanced when centrifuging. Also, please screw the top onto the micro-centrifuge during use.
Ask before you borrow something from someone else’s bench, and return it immediately after you’re finish using it.
If something breaks, please report it immediately!
Please keep the sinks and eye washes free of glassware, ice containers, etc.
If you don’t understand how to do something… ASK!
Tissue Culture Room
Always wipe down the hood with 70% EtOH when finished.
If you empty a Pasteur pipette container, please restock the hood with a new one. The same courtesy applies to Kimwipes, pipettes, etc.
Always turn off the vacuum pump when you’re finished in the hood.
If the biohazard bag is full, please empty.
If the liquid media waste bottle is extremely full (>1800 mL) please bleach it and dump it.
Lastly, please follow proper safety procedures and sterile techniques at all times.
Please keep the sinks and eye washes free of glassware, waste, etc.

## Slide 3: TC room notes
When you spill media in the TC hood or in the incubator, it's recommended that you first use water to wipe it up, then ethanol. The reason for this is that ethanol will not completely remove the salts from the surface, which can damage the surface and create spots. Have water handy in the TC room! Incubator shelves are removable for cleaning if necessary.
All media spills need to be cleaned up immediately. If you have a major media spill, I'm happy to help you clean it up (if I'm available). In the case of a "major spill", where media is spilled below the TC surface, or on a large area in an incubator, it should be cleaned right away and reported to me.
The hood is sterile due to YOUR TECHNIQUE, maintenance, and laminar flow.
Keep ONLY WHAT YOU NEED in the hood!

## Slide 4: UV lamp in the hood
Whenever using the UV lamps in the TC hoods, the blower should be turned off. If the blower is left on, the pressure behind the sash builds up and can potentially crack the sash. UV lamps are NOT recommended for sterilization of biosafety cabinets. However, as some protocols call for sterilization of certain surfaces, the following are guidelines for UV lamp use in all DAL TC hoods.
Feel free to use the UV light meter to determine how intense the lamp actually is.
Will is building a new UV light for chemistry for the lab.
1) Turn the blower off.
2) Lower the sash all the way before activating the UV light. 3) Leave the UV lamp on for no longer than 30 minutes. 4) When finished, raise the sash to the marked height & run the blower for 20 minutes before resuming work in the TC hood. **The blower should always be turned off when the sash is all the way down.** For more detailed information regarding UV sterilization, please see: 1) "At the bench a laboratory navigator" by Kathy Baker
2) http://dohs.ors.od.nih.gov/decontamination.htm
3) http://ehs.uky.edu/biosafety/uv_cabinets.html 4) Newsom SWB and BM Walsingham. 1974. Sterilization of the biological safety cabinet. J. Clin. Path. 27: 921-924.

## Slide 5: Working document for lab clean up items
Replace battery on -70
Clean up scale area
Clean up fume hoods
Organize the extra bulk boxes
Break down old boxes
Clean up and organize the TC room
Set up double flask in TC hood
Clean the TC hood
Clean the incubators
Clean up sink area
Organize the 4C, -20, and -70
Organize and label the lab drawers
Clean up, organize the MAGPix and plate reader areas
Clean up, organize the microscope room
Go through pipetters, any need servicing?

## Slide 6: Potential dates for lab-wide cleanup
Expect that this will run from 9a-5p
Grad students attendance mandatory (all day)
Schedule experiments around this time
Lunch provided (what do you want?)
Undergrads can come help when they can
Possible dates:
  Friday, 2/1
  Friday 2/8
  Monday 2/11
  Friday 2/15
  Monday 3/1

## Slide 7: Group Meeting Schedule
Jan 23 - Lab cleanup organizational meeting. Shelly and Dannielle
Jan 30 - Will
Feb 6 - Thuy
Feb 13 - Dannielle
Feb 20 - Lauren B
Feb 27 - Lauren J
Mar 6 - Thuy, Technique Review of MAGPix Assays
Mar 13 - Will, Technique Review of making an adenovirus
Mar 27 - Dannielle, JClub review of epigenetics in cancer progression
Apr 17 - Lauren B, JClub review of chemotherapeutic treatment options for triple negative breast cancer
Apr 24 - Lauren J, Technique Review of 3D PEG hydrogels