## Slide 1: Parallel gene synthesis in a microfluidic device by David Kong et. al
Presented by
Eric Gomez & Dahlia Alkekhia
December 2nd, 2010

## Slide 2: Background
Needed in the field: synthesize custom de novo long DNA strands and genes
Issues: accuracy, time, COST
  $0.1 per nucleotide for conventionally synthesized oligos
  $0.65 – $1.10 per bp for custom gene synthesis services
  Example: synthesis of bacterial genomes 106bp in size become prohibitively costly, requiring on the order of $100, 000 in oligos alone
Proposed technology:
Multi-chambered microfluidic device
Notes: Other important applications for de novo gene synthesis in biomedical research and biotechnology range from the cloning of individual genes to the development of synthetic DNA vaccines (2), vectors for gene therapy (3), and gene libraries for protein engineering and molecular evolution (4).
with the major expenditure components for such long syntheses being attributable to reagent and sample handling, synthesis of long genes of designed sequences for designated functions becomes possible

## Slide 3: Why?
minimize reaction volumes 50uL  500nL
Reduces sample handling and need for robotic handlers
Enables large number of complex reactions to be preformed in parallel
 reduces costs!
Reduces error
Notes:  reduce reagents and required starting oligonucleotide concentrations

## Slide 4
The Tiny Reaction : PCA
- Starting pool of
construction oligos
- Thermocycling leads to
annealing and extension
by DNA polymerase
- Multiple thermocycling
leads to increasingly
extended gene sequences
- Complete gene is achieved,
amplification can be
performed

## Slide 5: The Tiny Device
PDMS1
PDMS2
PDMS3
Fabrication
Blue & Green: Gene Synthesis Chamber
Yellow: Water Jacket
Blue: Fluid Inlet Channel
Red: Valve Channel

## Slide 6: Experimental Procedure
Genes selected:
  bacterial “alba” gene
  bacteriophage “hjc” gene
  GFP construct
  Red fluorescent protein (dsRed)
Every microfluidic reaction was also ran in vitro in normal PCR tubes to compare performance
All reaction products analyzed through PAGE
Mixes demonstrating successful synthesis amplified through PCR
Amplified products visualized again through PAGE to verify correct amplification
Products sequenced using amplifying primers to confirm correct gene
Errors quantified by vector cloning and transformation

## Slide 7: Results
(In PCR tubes)
IT WORKED!
With 50% higher yield relative to reactions in PCR tubes
Notes: The lower molecular weight species below the product bands indicate normal levels of assembly intermediates for a single reaction PCA
-how can you tell 50% high yield? Why was 750 circled?

## Slide 8: Error
Forty eight clones for both ‘in fluidic’ and in vitro DsRed synthesis yielded:
12.5% of full-length clones were error-free

## Slide 9: microarray
High density microarray-based method for synthesis of construction oligos
femtomoles or lower concentrations per sequence
microfluidic device architecture to enclose sets of oligo spots for gene synthesis
Cleave and collect
time
reagents
handling complex pools of oligos
money
introducing more error
Gene synthesis/ desired application
Insufficient
Incorporated into microfluidic device
Enough for gene synthesis in same device
amplification

## Slide 10: Looking ahead
Incorporation of existing DNA error correction techniques on-chip.
integration of in vitro protein expression using high quality synthetic DNA as a template.
assembly of constructs larger than single genes can be achieved with microfluidic devices, employing the same types of hierarchical in vitro assembly reactions used to create 12kb and larger segments

## Slide 11
Thank You!