## Slide 1: Optimal Feed Rate for Maximum EtOH Production
Conor Keith
Loyola Marymount University
March 2, 2016

## Slide 2: Outline
Chemostats and industrial ethanol manufacturing
Saccharomyces cerevisiae and the fermentation process
The role of glucose feed concentration in the fermentation process
A mathematical model of EtOH production in a chemostat environment
Maximization of EtOH production using free final time optimal control problem
Optimal feed flow rate

## Slide 3: How Ethanol is produced on the industrial level
Ethanol fermentation produces ethanol for use in food, beverages, and fuel.
Yeast convert sugars, like glucose, into cellular energy .
Ethanol and carbon dioxide are by products of this process.
Fermentation occurs in large fermentation tanks.
The enzyme alpha-amylase is added to tanks to break down corn starch into shorter carbohydrate chains called dextrins.
During saccharification process the enzyme glucoamylase is added to mixture to break down dextrins into glucose.
Starch is converted to simple sugars, yeast is added to convert glucose into ethanol and carbon dioxide. https://www.osha.gov/dts/osta/otm/otm_iv/descriptions.pdf

## Slide 4: Chemostats Can Be Used to Model Industrial Ethanol Production
Chemostat cultures have been used by researchers as a tool to simulate the different stages of industrial ethanol production.
Chemostat cultures allows scientists to gather data regarding metabolic processes of yeast cells

## Slide 5: Outline
Chemostats and industrial ethanol manufacturing
Saccharomyces cerevisiae and the fermentation process
The role of glucose feed concentration in the fermentation process
A mathematical model of EtOH production in a chemostat environment
Maximization of EtOH production using free final time optimal control problem
Optimal feed flow rate

## Slide 6: Saccharomyces cerevisiae is the most relevant yeast strain in Ethanol production
Saccharomyces cerevisiae is commonly used in winemaking, banking and brewing
S. cerevisiae perform the most common type of fermentation
Ethanol becomes toxic to yeast cells at high concentrations
S. cerevisiae is a preffered yeast strain due to its high stress tolerance and its ability to efficiently use carbon and nitrogen resources
Goal of industrial ethanol production is to produce maximum ethanol in shortest period of time
Most ethanol is produced in later stages, i.e. at or near zero growth rates and stationary phase

## Slide 7: The flexibility of Saccharomyces cerevisiae
S. cerevisiae can rapidly switch between respiratory and fermentative sugar metabolism in response to changes in availability of oxygen and fermentable sugars
S. cerevisiae can increase catabolic rates an start accumulating large amounts of ethanol upon this transfer
Glucose starved yeast can adapt when introduced to high glucose concentrations within minutes
Pathways responsible for fermentation process can suddenly catalyze sugar at very high rates, which is why S. cerevisiae is the most preferred yeast in industrial ethanol production (Van den Brink, et. al 2008).

## Slide 8: Outline
Chemostats and industrial ethanol manufacturing
Saccharomyces cerevisiae and the fermentation process
The role of glucose feed concentration in the fermentation process
A mathematical model of EtOH production in a chemostat environment
Maximization of EtOH production using free final time optimal control problem
Optimal feed flow rate
Conclusion

## Slide 9: The role of Glucose in Ethanol fermentation
Yeast contain enzyme called zymase which catalyzes fermentation process
Glucose zymase Ethanol + Carbon Dioxide
Glycolysis breaks down glucose to form pyruvate.
When oxygen is not present pyruvate undergoes fermentation.

## Slide 10: Outline
Chemostats and industrial ethanol manufacturing
Saccharomyces cerevisiae and the fermentation process
The role of glucose feed concentration in the fermentation process
A mathematical model of EtOH production in a chemostat environment
Maximization of EtOH production using free final time optimal control problem
Optimal feed flow rate

## Slide 11: A mathematical model of Ethanol Production in a Continuous Culture

## Slide 12: Parameters and Constants in Model
X = Cell mass concentration
S = Glucose concentration
P = Ethanol concentration
μ = Specific growth rate
π = Specific productivity
F = Feed rate
Notation used in Wang, et. al (1999)

## Slide 13: Parameters and constants continued
Growth equations from Wang, et. al (2008).

## Slide 14: Outline
Chemostats and industrial ethanol manufacturing
Saccharomyces cerevisiae and the fermentation process
The role of glucose feed concentration in the fermentation process
A mathematical model of EtOH production in a chemostat environment
Maximization of EtOH production using free final time optimal control problem
Optimal feed flow rate

## Slide 15: Brief Explanation of Dynamic Optimization
Goal: maximize objective function
State variable depends on control variable.
Decision maker chooses control variable at any given time
Road analogy

## Slide 16: A mathematical model of Ethanol Production in a Continuous Culture

## Slide 17: Optimal control of Fermentation Process
Goal is to find optimal feeding rate, feed concentration, initial glucose concentration, and initial volume such that the ethanol production rate is maximized at the minimum fermentation time.
The objective function is:
My model assumes initial values are fixed.

## Slide 18: Optimal Paths of State Variables

## Slide 19: Results from other research

## Slide 20: Values for optimal feeding rate and final time
Optimal final time for my simulation was about 65 hours and the maximum ethanol production was 20,836.842 grams.
Values are similar to values obtained by previous researchers using a similar model but with higher number of collocation points.
The feed rate concentration had an optimal path similar to the paths found in other research.
Once EtOH concentration hits a critical point, biomass decreases sharply towards initial point, but EtOH continues to increase.
This is consistent with (paper), which states that most EtOH is produced in the later stages of fermentation.

## Slide 21: Conclusion
Under the model I selected, maximum ethanol production is attained by adjusting feed rate concentration of glucose according to optimal path determined by solution to control problem.
EtOH concentration increases despite decreases in biomass concentration of yeast.
Feed rate and EtOH concentration are both constrained by total volume of chemostat/reactor.

## Slide 22: Acknowledgments
I would like to thank Dr. Fitzpatrick, Dr. Dahlquist, and my fellow classmates.

## Slide 23: References
Brauer, M. J., Saldanha, A. J., Dolinski, K., & Botstein, D. (2005). Homeostatic adjustment and metabolic remodeling in glucose-limited yeast cultures. Molecular biology of the cell, 16(5), 2503-2517.
Van den Brink, J., Canelas, A. B., Van Gulik, W. M., Pronk, J. T., Heijnen, J. J., De Winde, J. H., & Daran-Lapujade, P. (2008). Dynamics of glycolytic regulation during adaptation of Saccharomyces cerevisiae to fermentative metabolism. Applied and environmental microbiology, 74(18), 5710-5723.
Wang, F. S., & Cheng, W. M. (1999). Simultaneous Optimization of Feeding Rate and Operation Parameters for Fed‐Batch Fermentation Processes. Biotechnology Progress, 15(5), 949-952.
Vázquez-Lima, F., Silva, P., Barreiro, A., Martínez-Moreno, R., Morales, P., Quirós, M., ... & Ferrer, P. (2014). Use of chemostat cultures mimicking different phases of wine fermentations as a tool for quantitative physiological analysis. Microbial cell factories, 13(1), 85.
Gabriel, E., & Carrillo, U. (1999). Optimal control of fermentation processes (Doctoral dissertation, PhD Thesis, City University, London).
Banga, J. R., Balsa-Canto, E., Moles, C. G., & Alonso, A. A. (2005). Dynamic optimization of bioprocesses: Efficient and robust numerical strategies. Journal of Biotechnology, 117(4), 407-419.